## Slide 1
Lecture 10: Diodes
1. p-n junction
The conductivity of a semiconductor (silicon) is enhanced by doping.
Doping with a donor material (phosphorus) creates an n-type semiconductor, which has negative charge carriers (the extra electrons).
Doping with an accepter material (boron) creates a p-type semiconductor, which has positive charge carriers (the holes).
A p-n junction is made when a crystal has both types of doping. It is called a diode.
Nature diffusion of the electrons creates a depletion region in the p-n junction. Space charges are created in this region, which produce an internal electric field pointing from N to P.
The internal electric field prevents further diffusion. It produces a potential barrier for the electrons.
At 25 °C, the potential barrier in Si junction is about 0.6 V. It is about 0.3 V in Ge.
E

## Slide 2
2. I-V curve of a diode
Like all other electronic components, a diode is characterized by its I-V curve.
When the diode is forward-biased, the internal potential barrier is reduced, which allows electrons to flow.
When the diode is reverse-biased, the internal potential barrier is enhanced, which prevents electrons to flow.
At normal forward-biased use, Si diode has about 0.6 V drop across it. Ge diode has about 0.3 V.
÷50
×100
Without breakdown, the current I flowing through the diode can be approximated by an exponential function:
I0: Reverse saturation current
e: Charge of electron
V: Applied voltage
k: Boltzmann constant
T: Temperature
Further approximations:
1) When V > 100 mV,
Dynamic resistance
2) When V < -100 mV,

## Slide 3
3. Zener diodes
Zener diodes are manufactured with controlled reverse breakdown properties. They are designed to operate at or about their reverse breakdown voltage (Zener voltage, VZ), typically 2 V to 200 V.
Example 1: Simple Zener diode voltage regulator
The circuit is working at the reverse breakdown of the Zener diode. Even though Vin may vary somehow, the load voltage on RL is stabilized at VZ. Zener diodes can be used in series to obtain desired VZ .
Vin
RL
R
Example 2: The diode clipper
In the circuit the input voltage varies in both polarities. The output voltage on RL is clipped to the range of –VZ2 <Vout< VZ1.
Vin
R
RL
Z2
Z1

## Slide 4
RL
4. Rectification and power supply
1) Half-wave rectifier
The input is an alternating sinusoidal voltage. The diode only passes the positive voltages.
2) Full-wave rectifier
A bridge rectifier is used to rectify the secondary voltage of a transformer. The output is a positive full wave.
RL
3) Power supplies
Filter capacitors and IC voltage regulators are used to provide a stable DC voltage.

## Slide 5
Homework:
Ch3: 3,5