## Slide 1
Lecture 11: Transistors
1. Bipolar junction transistor
Bipolar junction transistors can be of either NPN or PNP type. They are used for amplification or switching.
In an NPN transistor, the base (B) and the collector (C) are lightly doped. The emitter (E) is heavily doped. The base is thin. The main charge carriers are the electrons.
The E-B junction is forward-biased, while the B-C junction is reverse-biased.
Electrons are injected from the emitter lead. Most electrons (99%) get into the collector. Only few electrons (1%) exit from the base lead.
P
N
N
B
E
C

## Slide 2
In an amplification application, a transistor is specified by its current gain
It is also known as hFE, and is almost a constant. Usually 10 < b < 500.
2. Characteristic curves of a transistor
A typical characteristic curve for a bipolar transistor shows the collector current Ic versus collector-emitter voltage Vce , with the base current Ib as a parameter.
Three regions on the characteristic curve:
Linear active region: Ic = b Ib , used for amplification.
Saturation region: reduced Ic increasement at larger Ib’s.
Cutoff region: Ic falls to zero because Ib is small.

## Slide 3
3. Transistor switch
Vout
This load line is drawn on the transistor characteristic curve to analyze the circuit.
Transistor cutoff and saturation can be used as a switch.
If V1= 0 then Ib = 0. The solution on the load line shows Ic = 0 and Vce= Vcc.
A high V1 (e.g., V1= 5 V) makes Ib large. The solution shows Ic is large (≈ Vcc /Rc) and Vce is small.
This switch is an voltage inverter: a high (low) voltage input at the base causes a low (high) voltage output at the collector.

## Slide 4
Homework:
Ch4: 1

## Slide 5
Lecture 12: Transistor amplifiers I
1. Universal DC bias circuit
Before discussing AC amplifiers, we first keep the transistor operating in the middle of the linear active region. This is the universal DC bias circuit. It sets the DC operating conditions for an amplifier.
Other bias circuits can be derived from the universal one by setting a resistor value to zero or infinity.
We first replace the left half of the circuit by its Thevenin equivalent:

## Slide 6
The universal DC bias circuit is now redrawn.
Our goal is to determine Ib , Ic and Vce . They work together to define the operating point (also called the quiescent point or Q point) of the transistor. The operating point is usually on the middle of the load line.

## Slide 7
2. Black box model of an amplifier
Zin is the impedance seen when looking into the input of a circuit. It gives us an idea of how much current can be drawn into the input of a device.
Zout refers to the impedance looking back into the output of a device. The output of a circuit is equivalent to a Zout in series with a voltage source.
When transmitting a signal, Zin of a device should be much higher than Zout.
A general amplifier can be represented by a black box.
Four black box parameters that specify the amplifier:
1) Voltage gain . (Open-loop voltage gain )
2) Current gain
3) Input impedance
4) Output impedance
Vout

## Slide 8
Homework:
Ch4: 2

## Slide 9
1. AC equivalent circuit for transistors
We now model a transistor’s response to an AC input around a given DC operating point. We use lower-case letters for AC currents and voltages, so
1) For the B-E junction,
2) For the C-E part,
Lecture 13: Transistor amplifiers II

## Slide 10
Based on and , the AC equivalent circuit for the transistor
is now

## Slide 11
2. Common-emitter amplifier
A common-emitter amplifier provides a voltage gain for the input signal.
The central part of this circuit is the universal DC bias circuit, which sets the DC operating point (Q point) for the circuit.
AC signals are added through C1 and extracted through C2.
AC analysis of an amplifier can be broken down into 3 steps. They are good mental stamina tests for physicists. Redraw the circuit when proceeding.
1) Treat the coupling capacitors as shorts. Treat the DC power supply as ground.

## Slide 12
2) Insert the AC equivalent circuit for the transistor. Simplify the circuit.

## Slide 13
3) Write vin, vout, iin, and iout in terms of ib. Compute a, g, Zin and Zout.

## Slide 14
3. Common-collector amplifier
A common-collector amplifier is also called an emitter follower, in which vout follows vin. It has a high input impedance, and a low output impedance. It thus provides a current gain. The circuit requires less power from a signal source to drive a load, compared to the case when the load is directly powered by the source.
AC analysis step 1:
Step 2:

## Slide 15
Step 3:

## Slide 16
Homework:
Ch4: 5,7,9