## Slide 1
The basic operation of the op-amp is:
AOL is the open-loop voltage gain, which is usually huge (104-109). Therefore, Vout may be quickly saturated. In reality Vout can only be within a range set by two saturation voltages:
Here
Lecture 14: Op-amps I
1. Op-amps
Op-amps are the short name for operational amplifiers. They are based on differential amplifiers constructed from normal transistors. This differential amplifier amplifies the voltage difference between the two inputs with a very large voltage gain.
An op-amp is usually packaged as an integrated circuit with multiple pins. We will treat the device as a black box, and learn some basic rules for its application.
An op-amp has two power supply voltages, Vcc+ and Vcc-. These two voltage sources are often omitted in a circuit diagram.
There are two signal inputs: the inverting input (-), and the non-inverting input (+). The two signs do not specify the polarity of voltages.

## Slide 2
2. Non-linear application: comparator
Because AOL is large, any small difference between the op-amp inputs will cause the output to saturate. For example, for AOL = 200k, at ±15 V power supplies, only a 70 μV difference between the two inputs makes the output saturate.
In the comparator circuit below,
When Vin is above 1V (reference voltage), the output swings to its positive saturation limit.
When Vin is below 1V, the output falls to its negative saturation limit.

## Slide 3
3. Golden rules of ideal linear op-amp operation
In linear applications, the circuits are characterized by a feedback connection from the output to the inverting input of the op-amp. The circuits can be analyzed by applying two approximate rules called the golden rules of ideal linear op-amp operation.
Rule #1: The output will do whatever is necessary to make the voltage difference between the inputs zero.
Rule #2: No current flows into the inputs.
3. Inverting amplifier
 Op amps are much easier than transistors in application.

## Slide 4
Homework:
Ch6: 1,2,5

## Slide 5
Lecture 15: Op-amps II
1. Non-inverting amplifier
2. Buffer (voltage follower)
This can be used between a high impedance voltage source and a low impedance load to alleviate loading due to the voltage divider effect.

## Slide 6
3. Adder
4. Differential amplifier

## Slide 7
5. Integrator
6. Differentiator
7. Current-to-voltage converter
R
Vout
Iin

VR

## Slide 8
Homework:
Ch6: 6,7,8,9